## Slide 1: A regression-based modelling approach for accurate dynamic power estimation in digital circuits
16/01/2023
Monticelli, D. – Student ID: 1610228
Electrical engineering – Electronic systems group
Notes: Welcome everybody, thank you for joining both here in this room and remotely.

## Slide 2: Introduction (1)
As Moore’s law (1965) drives technology scaling…
Major design constraint:
power dissipation
…from where power dissipation originates?
… The mo(o)re transistors per unit of area
Result: unbearable power density rise in a small chip area
Notes: -The semiconductor…
-Moore’s law depicts a trend for transistor scaling
-Higher speed, higher power

## Slide 3: Introduction (2)
Static: Due to parasitic, tech-dependent
Dynamic: charging/discharging capacitive load
Pdyn = Energy per transition × switching activity
Where:
E = Energy [J] f = frequency [1/s]
P = Power [J/s] = load [F]
α = activity factor = supply [V]
Energy =
Technology
input stimulus (ie: simulation)
Notes: -Power can be divided in 2:
-Vdd, f_ck known (we see how P and f_ck are linked)
-CL is given by tech, alpha input stimulus
-Today’s designs have billion transistors, so this solution does not scale well. To deal with this huge variable space, engineers build abstraction layers to reduce it

## Slide 4: Introduction (2)
Static: Due to parasitic, tech-dependent
Dynamic: charging/discharging capacitive load
Where:
E = Energy [J] f = frequency [1/s]
P = Power [J/s] = load [F]
α = activity factor = supply [V]
Technology
input stimulus (ie: simulation)
Abstractions!
Pdyn = Energy per transition × switching activity
Energy =

## Slide 5: Introduction (3)
Algorithmic (behavioural)
RTL (structural)
Logic synthesis (netlist)
Physical synthesis (placed netlist)
Sign-off & tape out (on chip measure)
Time (simulation + effort)
~minutes
Conflicting trends:
Fast estimations are inaccurate
Accurate estimations take time
~hours
~days/weeks
~weeks/months
~months/years
Need to meet strict power constraints by:
Explore design choices (DSE);
Being accurate
Notes: -So here we have a simplified version of a design flow
-algorithmic->functionality;
-RTL: functionality but aware of the signals switch
-synthesis: maps the functionality into gates with knowledge on the parasitics
-Timeline is indicative
-Need: evaluate different choices and be accurate
-Conflicting trends

## Slide 6: Introduction (4) Problem statement
    Prior art:
      Accurate and slow;
      Fast but inaccurate (no )
      Not generic solution (fixed implementation)
    This work:
      Fast, by reducing variable space;
      Accurate, from realistic and ;
      Generic solution with a component-based approach
Notes: -Existing work is either accurate but slow (large design space)
-Or fast and inaccurate , or do not provide a generic solution.
This work tries to overcome such limitation

## Slide 7: Literature overview (1)
Algorithmic (behavioural)
RTL (structural)
Logic synthesis (netlist)
Physical synthesis (placed netlist)
Sign-off & tape out (on chip measure)
Time (simulation + effort)
~minutes
~hours
~days/weeks
~weeks/months
~months/years
Conventional tools (eg: Joules):
Post-synthesis accuracy
Time consuming for design space explorations
Simulation-based () research topics:
Analytical
Regression-based
Notes: What does it mean to be accurate?
-Industry tools at this level would synthesize, simulate and run power for each design flavor, which takes time
-In the research, there are 2 main ways to approximate switching activity factor: analytical and regression-based

## Slide 8: Literature overview (2)
Analytical approach (α from action count)
Common drawbacks:
Action based (no activity involved)
Complex C++ libraries
Common benefits:
- Hierarchical approach based on OO models
- Fast power estimation
Tech parameters (C/C++)
Config. File (user input)
Power model
Performance simulator
action count
workload
Analytical tool
Estimated power
Notable examples
McPAT for CPUs
DSENT for NoCs
Notes: -We feed the tool with libraries that model parasitics and hardware configuration
-then we do not track activity but action counts
-From the technology model and how much a resource is accessed, power is retrieved
-pro/cons

## Slide 9: Literature overview (3)
Common benefits:
Accurate results for selected workloads
Fast estimation time
Common drawbacks:
Extended cycle-accurate training times
Power model fixed to hardware implementation (preventing DSE)
Regression-based (α from proxy activity)
Examples:
Yukai et al. : L1 regularization for feature selection
Apollo : L1 for selection L2 for relaxation
From Apollo paper
Notes: -Regression-based approaches use real activity factors but from few selected signals (proxies)
-To select those signals, simulations are run
-Signals that impact power the most are selected

## Slide 10: Literature overview (4)
  Analytical approach:
  Component’s action counts from performance simulator (eg: gem5) associated with power consumption
  Pruning approach:
  Prune and simulate few proxies representative of the whole design
+accurate
+real data traces
-Long trainings
-Fixed to hardware
Summary of related work
+Fast
+Hierarchical
-Actions
-Analytical
Notes: -Summary: we organized the work in a speed vs accuracy fashion.
-Analytical populate the top left because…
-Regression-based offer tradeoffs thanks to the various machine learning approaches
-Joules in an outsider

## Slide 11: This work (1)
Algorithmic (behavioural)
RTL
(cycle-accurate)
Logic synthesis (netlist)
Physical synthesis (placed netlist)
Sign-off & tape out (on chip measure)
Time (simulation + effort)
~minutes
This fast
This accurate
Objective:
approach to quantify early power estimation for power-aware design choices.
Bridge
the gap
~hours
~weeks
~weeks/months
~months/years
How to achieve this:
Implementation-independent (common) features
Average component’s input/output toggling activity
Regression-based
Position of this work
Notes: -Overall goal: accurate and fast enough to evaluate different design choices
-To do so: common features, avg in/out,
-We want to abstract the parasitic information and bring them at RTL level

## Slide 12: This work (2)
Extraction of generic features
Simulation based on average toggle activity coverage
Supervised training (activity -> power)
Notes: -Here on the right we can see the methodology flow to build the power model.
-It is divided in 2:
-Taking the structural RTL which is an interconnection of components

## Slide 13: This work (2)
Extraction of generic features
Simulation based on average toggle activity coverage
Supervised training (activity -> power)
Notes: -let’s see how these steps are performed in practice

## Slide 14: This work (3) Extraction of generic features
BW (4÷64) | IN (2÷4)
4 | 2
... | …
64 | 4
One design generated for each parameters combination
N:1 MUX
In this example: (64-4+1) x 3 = 183 design that will be synthesized
Notes: -feature extraction consist in finding some component’s parameters that are independent from the implementation
-Taking a simple component such as a mux, those can be…
-After we parametrize the design for each feature configuration, we can synthesize them

## Slide 15: This work (4) Simulation based on average toggle activity coverage
BW (4÷64) | IN (2÷4)
4 | 2
Clk
IN0
Sweeping input toggle rate: example with BW=4 and toggle_rate=25%
IN1
IN2
IN3
Benchmark generator
BW = 4
TR = 25%
0
0
0
0
Next
cycle
Notes: -Now for each synthesized design, we want to simulate it to see the power impact of our stimulus.
-To do so, benchmark generator
-it generates input vectors, given the BW and TR (explain TR)
-in this example, it means 1 bit per cycle
-From the animation, we see that on average we are toggling 25% of the bits, and this is done for each configuration

## Slide 16: This work (4) Simulation based on average toggle activity coverage
0
Clk
Sweeping input toggle rate: example with BW=4 and toggle_rate=25%
0
0
0
Benchmark generator
BW = 4
TR = 25%
1
0
0
0
IN0,3
IN0,2
IN0,0
IN0,1
BW (4÷64) | IN (2÷4)
4 | 2
Next
cycle

## Slide 17: This work (4) Simulation based on average toggle activity coverage
0
Clk
Sweeping input toggle rate: example with BW=4 and toggle_rate=25%
0
0
0
Benchmark generator
BW = 4
TR = 25%
1
1
0
0
0
0
0
1
IN0,3
IN0,2
IN0,0
IN0,1
BW (4÷64) | IN (2÷4)
4 | 2
Next
cycle

## Slide 18: This work (4) Simulation based on average toggle activity coverage
0
Clk
Sweeping input toggle rate: example with BW=4 and toggle_rate=25%
0
0
0
Benchmark generator
BW = 4
TR = 25%
1
1
0
1
0
0
0
1
1
0
0
1
IN0,3
IN0,2
IN0,0
IN0,1
BW (4÷64) | IN (2÷4)
4 | 2
Next
cycle

## Slide 19: This work (4) Simulation based on average toggle activity coverage
IN0,3
IN0,2
0
Clk
IN0,0
Sweeping input toggle rate: example with BW=4 and toggle_rate=25%
IN0,1
0
0
0
Benchmark generator
BW = 4
TR = 25%
0
1
0
1
0
0
0
1
1
0
0
1
1
1
0
1
BW (4÷64) | IN (2÷4)
4 | 2
Next
cycle

## Slide 20: This work (4) Simulation based on average toggle activity coverage
IN0,3
IN0,2
0
Clk
IN0,0
Sweeping input toggle rate: example with BW=4 and toggle_rate=25%
IN0,1
0
0
0
Benchmark generator
BW = 4
TR = 25%
0
1
1
1
0
0
0
1
1
0
0
1
1
1
0
1
1
0
1
0
BW (4÷64) | IN (2÷4)
4 | 2
Next
cycle

## Slide 21: This work (4) Simulation based on average toggle activity coverage
Clk
Sweeping input toggle rate: example with BW=4 and toggle_rate=25%
Benchmark generator
BW = 4
TR = 25%
IN0,3
IN0,2
IN0,0
IN0,1
0
0
0
0
0
0
0
1
1
0
0
1
1
1
0
1
1
0
1
1
1
1
0
1
1
0
0
1
0
0
1
0
1
0
0
0
BW (4÷64) | IN (2÷4)
4 | 2

## Slide 22: This work (5) Problems
Clk
IN0,3
IN0,2
IN0,0
IN0,1
0
0
0
0
0
0
0
1
1
0
0
1
1
1
0
1
1
0
1
1
1
1
0
1
1
0
0
1
0
0
1
0
1
0
0
0
Notes: 2 problems arise

## Slide 23: This work (5) Problems
Clk
IN0,3
IN0,2
IN0,0
IN0,1
0
0
0
0
0
0
0
1
1
0
0
1
1
1
0
1
1
0
1
1
1
1
0
1
1
0
0
1
0
0
1
0
1
0
0
0
Bit position impacts power consumption
0000
0001
0010
0100
1000
0000
1001
1001
0000
Benchmark generator
BW = 4
TR = 25%
Solution:
random interleaving
Notes: -MSB and LSB

## Slide 24: This work (5) Problems
Clk
IN0,3
IN0,2
IN0,0
IN0,1
0
0
0
0
0
0
0
1
1
0
0
1
1
1
0
1
1
0
1
1
1
1
0
1
1
0
0
1
0
0
1
0
1
0
0
0
Bit position impacts power consumption
Bitwidth granularity does not allow every toggle rate
Solution: Combination of the two granularities until convergence
Benchmark generator
BW = 4
TR = 30%
Notes: -We want to sweep from 1% to 100%, but what if our bitwidth resolution do not allow us to do so?

## Slide 25: This work (6) Summary
Take a component
Notes: In this work we use the average toggle activity at the component’s interface. At the beginning we said that the switching activity is the amount of times a net toggles. Here we take how many times on average the input and output of a component toggle. We will lose accuracy, because the internal nets are way more that the input and output bitlines, but this is the cost for abstracting. However, the bet of this approach is that the interface activity is representative enough of the internal activity. This abstraction allows us to build a systematic way for data generation
Continuing the example of one of the 183 designs, for the sake of simplicity we take 2 input and 4 bitwidths.

## Slide 26: This work (6) Summary
Take a component
Extract features
BW (4÷64) | IN (2÷4)
4 | 2
4 | 3
4 | 4
5 | 2
5 | 3
5 | 4
… | …
64 | 4
Notes: In this work we use the average toggle activity at the component’s interface. At the beginning we said that the switching activity is the amount of times a net toggles. Here we take how many times on average the input and output of a component toggle. We will lose accuracy, because the internal nets are way more that the input and output bitlines, but this is the cost for abstracting. However, the bet of this approach is that the interface activity is representative enough of the internal activity. This abstraction allows us to build a systematic way for data generation
Continuing the example of one of the 183 designs, for the sake of simplicity we take 2 input and 4 bitwidths.

## Slide 27: This work (6) Summary
Take a component
Extract features
  Synthesize each configuration
Example for BW=4 and IN=2
Notes: In this work we use the average toggle activity at the component’s interface. At the beginning we said that the switching activity is the amount of times a net toggles. Here we take how many times on average the input and output of a component toggle. We will lose accuracy, because the internal nets are way more that the input and output bitlines, but this is the cost for abstracting. However, the bet of this approach is that the interface activity is representative enough of the internal activity. This abstraction allows us to build a systematic way for data generation
Continuing the example of one of the 183 designs, for the sake of simplicity we take 2 input and 4 bitwidths.

## Slide 28: This work (6) Summary
Take a component
Extract features
  Synthesize each configuration
    Simulate sweeping average input toggle activity
Notes: In this work we use the average toggle activity at the component’s interface. At the beginning we said that the switching activity is the amount of times a net toggles. Here we take how many times on average the input and output of a component toggle. We will lose accuracy, because the internal nets are way more that the input and output bitlines, but this is the cost for abstracting. However, the bet of this approach is that the interface activity is representative enough of the internal activity. This abstraction allows us to build a systematic way for data generation
Continuing the example of one of the 183 designs, for the sake of simplicity we take 2 input and 4 bitwidths.

## Slide 29: This work (6) Summary
Take a component
Extract features
  Synthesize each configuration
    Simulate sweeping average input toggle activity
    Simulate each input toggle activity multiple times with random initial states
0000
0001
0010
0100
1000
0000
1001
1001
0000
Benchmark generator
BW = 4
TR = 25%
Notes: In this work we use the average toggle activity at the component’s interface. At the beginning we said that the switching activity is the amount of times a net toggles. Here we take how many times on average the input and output of a component toggle. We will lose accuracy, because the internal nets are way more that the input and output bitlines, but this is the cost for abstracting. However, the bet of this approach is that the interface activity is representative enough of the internal activity. This abstraction allows us to build a systematic way for data generation
Continuing the example of one of the 183 designs, for the sake of simplicity we take 2 input and 4 bitwidths.

## Slide 30: This work (6) Summary
Take a component
Extract features
  Synthesize each configuration
    Simulate sweeping average input toggle activity
    Simulate each input toggle activity multiple times with random initial states
    Compute power (Joules)
Notes: In this work we use the average toggle activity at the component’s interface. At the beginning we said that the switching activity is the amount of times a net toggles. Here we take how many times on average the input and output of a component toggle. We will lose accuracy, because the internal nets are way more that the input and output bitlines, but this is the cost for abstracting. However, the bet of this approach is that the interface activity is representative enough of the internal activity. This abstraction allows us to build a systematic way for data generation
Continuing the example of one of the 183 designs, for the sake of simplicity we take 2 input and 4 bitwidths.

## Slide 31: This work (6) Summary
Take a component
Extract features
  Synthesize each configuration
    Simulate sweeping average input toggle activity
    Simulate each input toggle activity multiple times with random initial states
    Compute power (Joules)
Build labelled dataset
  Repeat for each feature’s configuration
  Repeat for each component
Notes: Now we have the labelled dataset to train ML

## Slide 32: Regression-based approach (1)
Linear
    Linear with mean square penalty
    Linear with lasso penalty
Notes: -The following regression algorithms are evaluated
-Linear regression with 2 different penalties: interpolation

## Slide 33: Regression-based approach (1)
Linear
    Linear with mean square penalty
    Linear with lasso penalty
  Decision tree-inspired
    Decision tree (DT)
    DT ensemble methods:
      Random forest (bagging): independent DT
      Extreme gradient (boosting): sequential DT
Notes: -Decision trees (iteratively divide the feature space and tries to find patterns in the form of binary decisions
-2 ensemble methods derived from DT:

## Slide 34: Regression-based approach (1)
Linear
    Linear with mean square penalty
    Linear with lasso penalty
Decision tree-inspired
    Decision tree (DT)
    DT ensemble methods:
      Random forest (bagging): independent features DT
      Extreme gradient (boosting): sequential DT
Support vector regression (SVR)
.
.
.
.
.
.
Notes: SVR: it works by finding the hyperplane (in this case line) that best separate the data

## Slide 35: Regression-based approach (2)
Components characterization of: multiplexer, adder and multiplier
Notes: -once we have the labelled data
-we can evaluate the ML algorithms

## Slide 36: Regression-based approach (2)
Components characterization of: multiplexer, adder and multiplier
Split dataset into training and testing

## Slide 37: Regression-based approach (2)
Components characterization of: multiplexer, adder and multiplier
Split dataset into training and testing
Cross-validation check to prevent overfitting

## Slide 38: Regression-based approach (2)
Components characterization of: multiplexer, adder and multiplier
Split dataset into training and testing
Cross-validation check to prevent overfitting
Grid-search for best hyperparameter tuning

## Slide 39: Regression-based approach (2)
Components characterization of: multiplexer, adder and multiplier
Split dataset into training and testing
Cross-validation check to prevent overfitting
Grid-search for best hyperparameter tuning
Regressor with best mean absolute percentage error (MAPE) is chosen
Where:
actual value
forecasted value

## Slide 40: Regression-based approach (3)
Purpose of a model is not to fit the data, but to sharpen the question (S. Karlin)
Notes: -On the left…
-On the right…
-Now we have chosen the algorithm, so we can apply the approach to a use case

## Slide 41: Experimental validation: FIR filter
Transposed FIR fitler components’ decomposition
(Mi = multipliers; Ai = adders; Qi ,Y = registers)
Characterization phase:
Average input/output toggle rate (1%-100%)
Bitwidth (8bit -32bit)
XGB supervised learning
Notes: -For a use case, we take a FIR filter which
-Here we have the structural decomposition, where we see 4 multipliers, …
-We characterize a multiplier, an adder a register
-We use xgb

## Slide 42: Experimental validation: FIR filter
Transposed FIR fitler components’ decomposition
(Mi = multipliers; Ai = adders; Qi ,Y = registers)
Run-phase:
Run arbitrary workload (RTL)
Parse activity and features
Instant power inference from activity
Do we achieve post-synthesis accuracy?
Notes: For the run phase, we simulate the workload, parse the activity at the interface of each component, and infer the power given the features. Then we compare it with the measure performed with industry tools.

## Slide 43: Experimental validation: FIR filter Results
Feed the
Notes: -Here we have the results for every component for the 8bit case for 3 different input activities.
-On the x axis, we have the components
-In red the reference number, in blue the estimation
-We see that the estimation follows the trend.
-For low activity, A and M underestimate, then higher
-Also multiplier increases more than the others but the model follows
-Register offset

## Slide 44: Experimental validation: FIR filter Results
Feed the
Notes: -For higher activities, we see the same trend, with multiplier the highest
-Now we lump all the components together in a single bar

## Slide 45: Experimental validation: FIR filter Results
Notes: -Sum the contribution of each component for different toggle rates to have a higher view of the design
-Again red components, Blue estimation And in green now we have the glue logic
-Glue logic is logic inferred in-between components when we synthesizing the whole design to ensure to meet physical requirements
-Analyzing the error in red (only the components) we see that it is much smaller than the previous
-Analyzing the error in green -> offset

## Slide 46: Experimental validation: FIR filter Limitations
Glue logic: it is inferred during synthesis of the final design
  the whole is greater than the sum of each (attributed to Aristotle)
Output activity: it takes part to the power consumption
…no way to exhaustively sweep output toggle activity
Control logic: it needs cycle-accurate information
384–322 BC
Notes: -Glue logic: total power is not only the sum of the components but also something in between, hence the quote can be applied to many fields, and from today also in digital electronics
-we deal only with stream processing applications

## Slide 47: Future work to improve the results
Weighted contribution: every bitline affacts power differently
Glitching: no all toggles are back-annotated
Hierarchy: how much is the power affected adding more hierarchies?

## Slide 48: Conclusion
  Analytical approach:
  Regression approach:
+accurate
+real data traces
-Long trainings
-Fixed to hardware
+Fast
+Hierarchical
-Actions
-Analytical
short!
generic!
Limitations:
Stream processing applications
Structural design
Only one case studied
Manual feature extraction
Github repo: https://github.com/damonti/Characterization
Notes: So to wrap up: we can see if what we did in comparison with other works the things we addressed. We did so by proposing a new approach that however added some limitations

## Slide 49: Questions?
Thank you!
Switching activity
Notes: Presentation in over. Thank you for your attention and bearing with me. I am open for questions.